- In accordance with Regulation 74, at least one (1) business day’s notice must be given to the council of the intended completion of all roof framing forming part of the building work and (including top and bottom chord restraints, bracing and tie-downs).

- The completed roof framing must not be concealed until after the expiration of two (2) clear business days after the notice of completion of roof framing has been received by the council.

- The applicable checklist must be completed by a registered building work supervisor who has inspected the work and must be provided to the council when giving notice of the completion of roof framing.

Note:

The above processes do not apply to a Class 10 building if it is not attached to any part of the roof framing of a building of another class.

The following items have been checked and comply with the approved documents:

| ITEM | Site Work | AS 4440-2004 Reference | Checked |
| --- | --- | --- | --- |
| 1 | Hip end framing: Loose timber or jack trusses | 5.2.1, 5.2.2 |  |
| 2 | Location of special loads: Solar heating, air con. HWS, other | 1.6 |  |
| 3 | Bottom chord clear of non-load bearing walls | 2.2.2 |  |
| 4 | Internal support/tie-down | 2.2.1 &3.7 |  |
| 5 | Fixing to tops of bracing walls - slotted brackets | Fig. 2.2 |  |
| 6 | Fixing to non-loadbearing walls – slotted brackets | Fig. 2.3 |  |
| 7 | Truss locations/orientation: Spacing, span | 3.1 |  |
| 8 | Truss bow (L/200 max) | Fig. 3.2 |  |
| 9 | Truss plumb (H/50 max) | Fig. 3.3 |  |
| 10 | Supplementary timber: ceiling trim | 3.5 & 3.6 |  |
| 11 | Truss Tie-Down requirements – as per approval | 3.7 |  |
| 12 | Fixing of multi-ply truss | 3.8 |  |
| 13 | Top Chord Bracing: Layout and Fixing – steel-brace | 4.1 |  |
| 14 | Steel-brace splice | Fig. 4.20 |  |
| 15 | Steel-brace end-fixing at apex | Fig. 4.21 |  |
| 16 | Steel-brace end-fixing at heel-to-top plate | Figs. 4.22 & 4.23 |  |
| 17 | Steel-brace at heel-to-girder truss | Fig. 4.24 |  |
| 18 | Steel-brace at cantilevers | Fig. 4.25 |  |
| 19 | Top Chord Restraint (spacing and fixing) | Fig. 4.1 |  |
| 20 | Intermediate Top Chord Ties (Valley Truss) | Fig. 4.2 |  |
| 21 | Fixing of Valley Trusses | Fig. 5.6 |  |
| 22 | Bottom Chord Restraint. Spacing and Size of Restraint | 4.4 |  |
| 23 | Web Tie/Web Brace | 4.5 |  |
| 24 | Bottom Chord Restraint Bracing | Fig. 4.28 |  |
| 25 | Truss-to-truss connections appropriate for wind speed: Hip Ends, Girder Trusses, Valley Trusses, Non Load-Bearing Walls | Section 5 |  |
| 26 | Girder Truss Position and Girder Boots | 5.3 |  |

Continued on page 3

Continued from page 2

| ITEM | Site Work | AS 4440-2004 Reference | Checked |
| --- | --- | --- | --- |
| 27 | Girder Truss Restraint |  |  |
| 28 | Overhangs: Eaves Detail (Supported, Not Supported) Structural or Non-Structural Fascia Verge Detail (Gable End Truss Supported on End Wall Or Free Spanning) Verandahs and Pergolas must not be attached to the ends of truss overhangs without specific design | Section 6 |  |
| 29 | Waling plate fixing | Fig 5.5 |  |
| 30 | Truss connection to timber/steel beams |  |  |
| 31 | Gable end framing | 6.2 |  |
| 32 | Truss modification/defects | 3.9 |  |
| 33 | Truss site suitability: corrosive environments | 3.10 |  |
| 34 | Advise on cornice fixing to Appendix B | B3 |  |
| 35 | Bearing Width to Appendix B | B4 |  |
| 36 | Steel roof battens, where used, must be legibly and durably marked with the reference AS 1397, the base steel thickness, and the designation of the steel base and coating |  |  |
| 37 | Timber trusses/roof framing were transported, stored, lifted and handled on the site in a proper manner and an area was provided on the site for their satisfactory storage | Appendix E of AS 4440 and/or Appendix H of AS 1684.2. |  |
| 38 | All trusses are appropriately marked by the fabricator so the fabricator can be identified and the particular truss can be located as per the approved layout plan. |  |  |
| 39 | Unless the roof framing has been designed otherwise, a label is provided on a truss immediately adjacent to the roof access hole, stating that the trusses have not been designed for additional loads such as attached carports/verandahs, a water heater, air conditioner or household storage; and that truss members must not be cut to fit building services. If the roof framing has been designed for additional loads, the trusses that are to support any additional load must be clearly identified. |  |  |

| Signature: |  |  | Date: |  |
| --- | --- | --- | --- | --- |

The following items have been checked and comply with the approved documents:

| ITEM | Site Work | AS 1684 Reference | Checked |
| --- | --- | --- | --- |
| 1 | Roof constructed in accordance with approved layout |  |  |
| 2 | Bracing | Section 8 |  |
| 3 | Coupled roof connections – ceiling joists to rafters, collar ties to rafters | 7.1.2.2 |  |
| 4 | Tie-downs | Section 9 |  |
| 5 | Transfer of wall frame bracing | 8.3.6.9 |  |
| 6 | Point loads - including beams, struts, are adequately supported |  |  |
| 7 | Location of special loads: Solar heating, air con, HWS, Other |  |  |
| 8 | Steel roof battens, where used, must be legibly and durably marked with the reference AS 1397, the base steel thickness, and the designation of the steel base and coating |  |  |
| 9 | Timber trusses/roof framing were transported, stored, lifted and handled on the site in a proper manner and an area was provided on the site for their satisfactory storage | Appendix E of AS 4440 and/or Appendix H of AS 1684.2. |  |
| 10 | All trusses are appropriately marked by the fabricator so the fabricator can be identified and the particular truss can be located as per the approved layout plan. |  |  |

| Signature: |  |  | Date: |  |
| --- | --- | --- | --- | --- |

The following items have been checked and comply with the approved documents:

| ITEM | Site Work | Checked |
| --- | --- | --- |
| 1 | Steel is legibly and durably marked with the reference AS 1397, the base steel thickness, and the designation of the steel base and coating |  |
| 2 | Hip end framing: jack trusses or hip trusses |  |
| 3 | Location of special loads: Solar heating, air con. HWS, Other |  |
| 4 | Bottom chord clear of non-loadbearing walls |  |
| 5 | Internal support/tie-down |  |
| 6 | Fixing to non-loadbearing walls – slotted brackets |  |
| 7 | Truss locations/orientation: Spacing, span, station |  |
| 8 | Truss, rafters, ceiling joists overall straightness (L/500 max) |  |
| 9 | Truss plumb (H/100 or 20 mm max) unless trusses designed to be installed out of plumb |  |
| 10 | Truss Tie-Down requirements – as per approval |  |
| 11 | Fixing of double truss |  |
| 12 | Top Chord Bracing: Layout and Fixing – steel-brace |  |
| 13 | Top Chord Restraint (spacing of purlin/tile batten) |  |
| 14 | Bottom Chord Restraint. Spacing and Size of Restraint |  |
| 15 | Web Tie/Web Brace |  |
| 16 | Truss-to-truss connections |  |
| 17 | Girder Truss Position and Girder Boots |  |
| 18 | Girder Truss Restraint. |  |
| 19 | Waling plate fixing |  |
| 20 | Truss connection to timber/steel beams |  |
| 21 | Gable end framing |  |
| 22 | Truss modification/defects |  |
| 23 | Truss site suitability: corrosive environments |  |
| 24 | All trusses are appropriately marked by the fabricator so the fabricator can be identified and the particular truss can be located as per the approved layout plan. |  |
| 25 | Unless the roof framing has been designed otherwise, a label is provided on a truss immediately adjacent to the roof access hole, stating that the trusses have not been designed for additional loads such as attached carports / verandahs, a water heater, air conditioner or household storage; and that truss members must not be cut to fit building services. If the roof framing has been designed for additional loads, the trusses that are to support any additional load must be clearly identified. |  |

| Signature: |  |  | Date: |  |
| --- | --- | --- | --- | --- |

The following items have been checked and comply with the approved documents:

| ITEM | Site Work | Checked |
| --- | --- | --- |
| 1 | Steel is legibly and durably marked with the reference AS 1397, the base steel thickness, and the designation of the steel base and coating |  |
| 2 | Roof constructed in accordance with approved layout |  |
| 3 | Bracing |  |
| 4 | Coupled roof connections – ceiling joists to rafters, collar ties to rafters |  |
| 5 | Tie-downs |  |
| 6 | Transfer of wall frame bracing |  |
| 7 | Point loads - including beams, struts, are adequately supported |  |
| 8 | Location of special loads: Solar heating, air con, HWS, Other |  |
| 9 | All trusses are appropriately marked by the fabricator so the fabricator can be identified and the particular truss can be located as per the approved layout plan. |  |

| Signature: |  |  | Date: |  |
| --- | --- | --- | --- | --- |

The following items have been checked and comply with the approved documents:

| ITEM | Site Work | Checked |
| --- | --- | --- |
| 1 | Where there are existing roof trusses – the nailplates are not separating or have not separated from the timber |  |
| 2 | Existing tie-downs and connections are in place and in good condition |  |
| 3 | Where the Class 10 structure is to be attached at or near an existing hip end, existing jack rafters and jack trusses are not separating from hip rafter or top chord of hip truss |  |
| 4 | Details are provided of any new strengthening, tie-down, connection or rectification work |  |

| Signature: |  |  | Date: |  |
| --- | --- | --- | --- | --- |